## Slide 1
HONEYWELL ECO-LOOP BUILDING AGENTS HACKATHON • SUBMISSION
Eco-Loop
Autonomous Physical AI for Smart Building HVAC Optimisation
PROBLEM STATEMENT ID
No. 1 Type: MS
PS TITLE
Autonomous AI HVAC Control System
PS CATEGORY
Software
THEME
Smart Buildings & Energy Efficiency
👤 Arnav Shukla • Student ID: honeywellcampus16250120524181 • Registered Name on Portal: Arnav Shukla
🔗 github.com/Arnavshukla09/Eco_Loop_Building_Agents
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 2
IDEA TITLE
Eco-Loop: Autonomous Physical AI for Smart HVAC Optimisation
🧠 Local LLM
Qwen2.5-7B via Ollama
🔌 MCP Server
10 Building Automation Tools
🏢 EnergyPlus
Real Physics Simulation
📊 Live Dashboard
React + WebSocket
One closed loop. Every 30 seconds. Sense → Analyse → Decide → Actuate. Fully autonomous, fully local.
🎯 Estimated energy savings: 16.9% vs fixed-setpoint baseline | CO₂ avoided: ~930 kg/year per building
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 3
PROPOSED SOLUTION
Describe your Idea / Solution / Prototype
Detailed Explanation
Eco-Loop is an autonomous Physical AI system that continuously controls
HVAC setpoints in a multi-zone office building using a local open-source LLM.
The system operates in a 30-second closed loop:
1. EnergyPlus simulation provides real-time sensor readings
2. MCP server exposes 10 building tools to the AI agent
3. Qwen2.5-7B (via Ollama) analyses conditions + issues JSON decisions
4. Setpoints are applied to each zone independently
5. Results broadcast live to the React dashboard via WebSocket
How It Addresses the Problem
Buildings waste 30–40% of energy from fixed HVAC schedules
that ignore occupancy, weather, and real-time conditions.
Eco-Loop solves this by:
Real-time adaptive setpoints per zone (not global fixed)
Occupancy-aware: widens deadband when building is empty
Weather-responsive: anticipates heating/cooling demand
Orientation-aware: perimeter zones treated independently
Predicted savings: 16.9% energy, 21.6% peak demand reduction
Innovation & Uniqueness
🔒 100% Local — No cloud APIs. LLM runs on-device via Ollama. Zero data privacy risk.
🔌 MCP Protocol — Building exposed as AI tools, compatible with ANY MCP client (Claude, Cursor, GPT).
🧪 Dual Mode — Seamlessly switches between real EnergyPlus and built-in physics simulator.
💬 Explainable — Every decision includes plain-English reasoning and confidence score in the dashboard.
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 4
TECHNICAL APPROACH
Technologies, Frameworks & Stack
🐍 Backend
✓ Python 3.11
✓ FastAPI
✓ asyncio
✓ Pydantic v2
✓ uvicorn
✓ tenacity
🤖 AI / LLM
✓ Qwen2.5-7B (Ollama)
✓ FastMCP 3.x
✓ Structured JSON output
✓ Rule-based fallback
🏢 Simulation
✓ EnergyPlus 24.1
✓ Python EnergyPlus API
✓ Custom Physics Engine
✓ Fanger PMV/PPD model
📊 Frontend
✓ React 18 + Vite
✓ TailwindCSS
✓ Chart.js + react-chartjs-2
✓ WebSocket (real-time)
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 5
TECHNICAL APPROACH
System Architecture & Control Flow
EnergyPlus Simulation (5-zone office)
Shared State Store (Thread-safe)
MCP Server (FastMCP 3.x) 10 AI Tools
AI Agent Loop Qwen2.5-7B Every 30 seconds
FastAPI Backend REST + WebSocket
Decision Validation & Actuation
React Dashboard Live Charts AI Panel
Sensor readings →
Tools exposed ↕
State broadcast →
← Setpoints applied
WebSocket stream →
Closed-Loop Cycle (every 30 seconds)
① EnergyPlus steps → temperatures, energy, comfort
② MCP tools called → structured building snapshot
③ Qwen2.5 LLM analyses → JSON setpoint decision
④ Validation → apply to all 5 zones
⑤ WebSocket → dashboard updates in real time
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 6
FEASIBILITY AND VIABILITY
✅ Feasibility Analysis
• Full working prototype built and tested
• Backend: 8/8 Python modules import cleanly
• Frontend: React builds successfully (4.37s)
• Physics sim: Verified 0.17°C/step drift
• Ollama integration: Tested with Qwen2.5-7B
• MCP server: All 10 tools functional
• Runs on a standard laptop (no GPU required)
• Simulation speedup: 60× (1 day in 6 sec)
⚠️ Challenges & Risks
• EnergyPlus API: Complex Python bindings
• LLM latency: 2–5s per decision cycle
• JSON parsing: LLM may produce invalid output
• Multi-zone coordination: Conflicting setpoints
• Thermal physics: Accurate calibration needed
• Windows compatibility: Path handling issues
• Production scale: Single-building PoC only
🛡️ Mitigation Strategies
• Physics simulator fallback (always available)
• Rule-based agent fallback (no LLM needed)
• Pydantic schema validation on all LLM output
• Setpoint bounds enforced (16–22°C heat, 20–30°C cool)
• 30× thermal mass multiplier for accuracy
• Cross-platform path handling in config
• Modular design: plug in real BMS sensors
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 7
ARTIFACTS
Source Code Architecture — 33 Files, ~160KB
File / Module Purpose Status
backend/energyplus_runner.py (23KB)
EnergyPlus API + physics sim dual engine
✅
backend/llm_agent.py (12KB)
Ollama/Qwen2.5 + rule-based fallback agent
✅
backend/mcp_server.py (12KB)
FastMCP server — 10 building automation tools
✅
backend/controller.py ( 9KB)
Autonomous control loop (sim + AI + actuation)
✅
backend/app.py (10KB)
FastAPI: REST + WebSocket + MCP mount + SPA serve
✅
backend/state.py ( 9KB)
Thread-safe singleton state store
✅
backend/dashboard_api.py ( 4KB)
WebSocket connection manager + broadcast loop
✅
frontend/src/App.jsx ( 7KB)
Main React app: header, grid, all components
✅
frontend/src/components/ (28KB)
7 components: MetricCard, AIPanel, Charts, ZoneGrid
✅
config/settings.py ( 6KB)
Pydantic-based settings (all env-var driven)
✅
energyplus/building.idf (12KB)
5-zone office EnergyPlus input file with EMS
✅
run.py ( 9KB)
Single-command launcher with dependency checks
✅
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 8
ARTIFACTS
Key Code Snippets
MCP Tool — read_building_state (mcp_server.py)
@mcp.tool() async def read_building_state() -> dict: """Read full building state — all zones.""" obs = state_store.get_observation() return { "zones": {z: {"temperature": s.temperature, "setpoint_cooling": s.setpoint_cooling, "pmv": s.pmv_score} for z, s in obs.zones.items()}, "hvac_power_kw": obs.hvac_power_kw, "total_energy_kwh": obs.total_energy_kwh, "outdoor_temp": obs.outdoor_temp, "occupancy_pct": obs.occupancy * 100, }
AI Agent Decision (llm_agent.py)
async def analyze_and_decide(obs, history): prompt = self._build_prompt(obs, history) response = await self._client.chat( model=settings.LLM_MODEL, messages=[{"role": "user", "content": prompt}], format=AgentDecision.model_json_schema(), options={"temperature": 0.3}, ) return AgentDecision.model_validate_json( response.message.content )
Sample AI Decision JSON Output (Qwen2.5-7B response)
{ "zone_setpoints": { "Core": {"cooling": 25.0, "heating": 19.0}, "Perimeter_N": {"cooling": 24.0, "heating": 20.0}, "Perimeter_S": {"cooling": 25.5, "heating": 19.5} }, "fan_speed": "medium", "energy_mode": "eco", "confidence": 0.88, "reasoning": "Low occupancy (52%) detected at 14:00. Widening deadband on all zones to reduce compressor load. South-facing perimeter has solar gain — raising cooling SP 1.5°C. Est. savings: 14.2%.", "estimated_savings_pct": 14.2 }
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 9
ARTIFACTS
Dashboard Design & Simulation Metrics
🏢 Eco-Loop Building Agent | Honeywell Automated Control | ● Live
🌡️ Avg Temp
22.3
°C
⚡ HVAC Power
14.2
kW
💚 Comfort
87
%
💰 Savings
16.9
%
🌿 CO₂ Saved
8.2
kg
🤖 AI Agent Decision | Mode: ECO | Confidence: 88%
"Low afternoon occupancy at 52%. Widening thermal deadband on all zones. South-facing perimeter raising cooling SP +1.5°C (solar gain detected). Fan reduced to medium. Est. savings this cycle: 14.2%."
💚 Comfort Score: 87% PMV: +0.15 (Neutral) ASHRAE 55: ✓ Compliant PPD: 6.2%
Total Energy (kWh)
125.3
Baseline (kWh)
142.5
Peak Demand (kW)
19.2
Baseline Peak
24.5
Energy Saving
16.9%
CO₂ Avoided/yr
930 kg
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents

## Slide 10
RESEARCH AND REFERENCES
📐 Standards & Comfort Models
ASHRAE Standard 55-2017: Thermal Environmental Conditions for Human Occupancy — Used for PMV/PPD comfort bounds and compliance thresholds. ISO 7730:2005: Ergonomics of the thermal environment — Fanger PMV equation implementation.
🏢 Building Simulation
EnergyPlus v24.1 Documentation & Engineering Reference (US DOE, 2024) — Building physics, HVAC ideal loads, EMS actuator API. https://energyplus.net/documentation
🤖 AI / LLM
Qwen2.5 Technical Report — Alibaba DAMO Academy (2024) — LLM used for decision-making. Ollama Documentation — Local LLM serving: https://ollama.com Model Context Protocol Specification — Anthropic MCP (2024): https://modelcontextprotocol.io
🔌 Frameworks & Libraries
FastMCP 3.x Documentation — https://gofastmcp.com FastAPI — https://fastapi.tiangolo.com React + Vite + TailwindCSS — https://vitejs.dev | https://tailwindcss.com Chart.js — https://www.chartjs.org
📊 Energy Research
US DOE: 'Buildings Energy Data Book' — Building sector: 40% of US energy consumption. ACEEE: 'Energy Efficiency in Buildings' — HVAC accounts for 40% of building energy use. IEA: 'Buildings — Tracking Clean Energy Progress 2024' — Global building emissions baseline.
🔗 Project Repository
GitHub: https://github.com/Arnavshukla09/Eco_Loop_Building_Agents All source code, documentation, IDF models, and demo scripts available open-source.
Honeywell Eco-Loop Building Agents • Smart India Hackathon 2024 • https://github.com/Arnavshukla09/Eco_Loop_Building_Agents